## Slide 1: Camso Creo Custom menus toolbars
Save as Step
Export active model in step and save it to C:\ptc\_step.
CAUTION:
Instead of using the …
Tool Tips
NOTE: Surf align only works with parts or assemblies created using Camso templates
3D menu
Surf align
Align selected surface parallel to the screen.
New DRW
Open Camso Drawing creator.
Open DRW
Using the 3D number will try to open a drawing in Windchill or in the working directory.
Edit Hole Note
Will open a text file where you can copy paste hole notes.
Color menu change the background colors
Create parameter
Generate default Camso parameters.
Fix Parameter.
Reads all parameters save their values, erase all parameters and recreate them with value.
Fix Parameter.
Merge current model parameters with Camso parameters and create missing parameters.
Close erase No Save.
Close active windows and erase not display.

## Slide 2
Save as Step
Export active drawing in selected format and save it to C:\ptc\_choosenformat
CAUTION:
Instead of using the …
Tool Tips
NOTE: Surf align only works with parts or assemblies created using Camso templates
2D menu
Replace Format
Function use to change the Drawing cartridge.
See: 0027-FormatReplace
Change DTL
Adjust drawing options as per Camso default values.
Edit Hole Note
Will open a text file where you can copy paste hole notes.
Change the decimal format for selected dimension.
Add a drawing sheet.
Will create a new sheet and run the replace format.
Delete Parameter.
Delete drawing parameters.
Add these symbol to selected dimension.